## Slide 1: Addition of Groundwater Targets to Freshwater SBTs v2
Technical Background

## Slide 2: Objective
Update v1.1 methodology to consider protection of groundwater
  v1.1 defined the amount of water use a company can have in a basin while being protective of environmental flow requirements
  v2 will define the amount of water use a company can have in a basin while being protective of environmental flow requirements and groundwater levels

## Slide 3: Overview of Changes to v1.1 Steps
Calculate baseline water use
Select model
Assess required percent reduction in water use
Set targets
Notes: The focus of this slide deck is to describe changes between v1.1 and v2.

## Slide 4: Overview of Changes to v1.1 Steps
Calculate baseline water use
  Disaggregate baseline to distinguish whether water supply comes from surface water and/or groundwater
  Underlying theory is that protection of groundwater levels must be achieved via reduction in groundwater use
Select model
Assess required percent reduction in water use
Set targets

## Slide 5: Overview of Changes to v1.1 Steps
Calculate baseline water use
Select model
  If a groundwater management plan exists, use it as the basis for setting targets
  If no management plan exists, use global model (if appropriate)
Assess required percent reduction in water use
Set targets
Notes: Simpler approach than used for protection of stream flows because we are not requiring companies to see out and apply local models developed outside of an authorized management plan.

## Slide 6: Overview of Changes to v1.1 Steps
Calculate baseline water use
Select model
Assess required percent reduction in water use
  Define environmental threshold
    Maintain stable aquifer levels into the future
    Maintain aquifer levels within the root zone for groundwater-dependent ecosystems
  Process global model results
Set targets

## Slide 7: Overview of Changes to v1.1 Steps
Calculate baseline water use
Select model
Assess required percent reduction in water use
  Define environmental threshold
    Maintain stable aquifer levels into the future
    Maintain aquifer levels within the root zone for groundwater dependent ecosystems
  Process global model results
Set targets

## Slide 8: Steps to Processing Global Model
Run global groundwater model (presumably GSGM) for a range of global pumping reduction scenarios (e.g., 0%, 10%, …, 90%, 100%)
  Model outputs aquifer elevation over time at hi-resolution grid
Assess percent reduction in pumping necessary to achieve stable aquifer levels per grid cell
  Consider groundwater dependent ecosystems, as appropriate
Spatially average reduction percentages across Pfafstetter Level 5 basins

## Slide 9: Hypothetical Model Result for Status Quo (0% Reduction) Monotonically Decreasing Aquifer Level
Status quo is unacceptable because groundwater levels continue to drop into the future

## Slide 10
Hypothetical Model Result for 10% Reduction in Pumping Monotonically Decreasing Aquifer Level
10% reduction in pumping is also unacceptable because groundwater levels continue to drop into the future, albeit at a slower rate of decline

## Slide 11
Hypothetical Model Result for 20% Reduction in Pumping Dynamically Stable Aquifer Level
20% reduction in pumping is acceptable (for non-groundwater dependent ecosystems) because it results in dynamically stable water levels

## Slide 12
Groundwater-Dependent Ecosystem Example
Dynamically Stable Aquifer Level (but Beneath Max Root Zone Depth)
20% reduction in pumping is not acceptable for this groundwater-dependent ecosystems because the dynamically stable water level is beneath the root zone depth

## Slide 13
Groundwater-Dependent Ecosystem Example
Dynamically Stable Aquifer Level Consistent with Max Root Zone Depth)
A 30% reduction in pumping is required for this groundwater-dependent ecosystems because the dynamically stable water level is within the root zone depth

## Slide 14: Steps to Processing Global Model
Run global groundwater model (presumably GSGM) for a range of global pumping reduction scenarios (e.g., 0%, 10%, …, 90%, 100%)
  Model outputs aquifer elevation over time at hi-resolution grid.
Assess percent reduction in pumping necessary to achieve stable aquifer levels per grid cell
  Consider groundwater-dependent ecosystems, as appropriate
Spatially average reduction percentages across Pfafstetter Level 5 basins

## Slide 15
Spatially Average Reduction Percentages Across Pfafstetter Level 5 Basins
Model outputs at high resolution grid
Repeat model output processing described above for each grid cell
Spatially average reduction percentages across Pfafstetter Level 5 basins

## Slide 16: Changes to v1.1 Steps
Calculate baseline water use
Select model
Assess required reduction in water use
Set targets
  Target depends on pathway and type of basin

## Slide 17: Questions for Reviewers
Spatially average reduction percentages across Pfafstetter Level 5 Basins or base reduction on grid cell with largest required reduction?
Do we consider response time when restoring a degraded groundwater-dependent ecosystem?
**Find all consultation questions in the survey on the Freshwater V2 public consultation landing page

## Slide 18
Spatially Average Reduction Percentages Across Pfafstetter Level 5 Basins (or Choose Most Restrictive)?
It may be worthwhile to examine variability in GSGM results prior to deciding

## Slide 19: Do We Consider Response Time When Restoring a Degraded Groundwater-dependent Ecosystem?
It may take decades to achieve a dynamically stable aquifer level

## Slide 20: Do We Consider Response Time When Restoring a Degraded Groundwater-dependent Ecosystem?
It may take decades to achieve a dynamically stable aquifer level
Response time can be shortened by selecting a larger reduction percentage